Physics Problems 6 d

Name_______________________

- A net force of 55 N acts due west on an object.  What added single force on the object produces equilibrium?

- Two forces act on an object.  One force is 6.0 N horizontally.  The second force is 8.0 N vertically.

  - Find the magnitude and direction of the resultant.

  - If the object is in equilibrium, find the magnitude and direction of the force that produces equilibrium.

- A 62 N force acts at 30.0° and a second 62 N force acts at 60.0° .

  - Determine the resultant force.

  - What is the magnitude and direction of the force that produces equilibrium?

- Two forces act on an object.  A 36 N force acts at 225°.  A 48 N force acts 315°.  What would be the magnitude and direction of their equilibrant?

- The 168 N sign is hung by ropes that each make an angle of 42° with the horizontal.  What force does each rope exert?

- The people who hung the sign decided to raise it higher by pulling the two ropes more horizontal.  They increased the force on each rope to 575 N and keep the angles equal.  What angle does each rope make with the horizontal now?

Answers:

- 55 N due east

- a.  10.0 N, 53°    b.  10 N, 233°

- a.   120 N 45°     b.  120 N 225°

- 60N @ 278°

- 126 N

- 8.4°