Electricity- movement of electrons

- Electric Charge when an object gains electrons or loses electrons it is said to be charged.

  - Two types of charges

    - Positive (+)

    - Negative (-)

      - Opposite charges attract

      - Like charges repel

  - Static electricity is electric charge built up in one place

  - Any charged object has an electric field around it

    - An electric field exerts a force on anything that has an electric charge

  - Static discharge is the loss static electricity into something else

    - lightening is and enormous electrical discharge

      - the cloud becomes negatively charged because of the redistribution of water

      - The bottom of the cloud will be negative and the top of the cloud will be positive

- Conduction is electrons moving

  - Conductor is some thing that transfers electrons.

    - metals tend to be good conductors

  - Insulator is a substance that doesn’t let electrons move through it

    - Nonmetals tend to be good insulators

  - The earth is a large body that can absorb a large amount of electric charge

    - This is why there is a ground used in your house

- Electroscope is a device used to detect an electric charge (page 596)

- Current is the movement of electrons or charges

  - Charges are measured in Coulombs

    - A coulomb is 6x1018 electrons

  - One measurement of electricity is the coulombs that flow through a wire each second

    - The unit for this measurement is the ampere

    - 1 amp = coulomb/second

  - There are several ways that current can be produced

    - Wet cell battery

    - Dry cell Battery

    - Generator

  - There is two types of current

    - Direct current (DC) is electricity that flows steadily in one direction

      - An example is how electricity flows from a battery

    - Alternating current (AC) is produced when the current is changing direction over and over

      - An example of this would be what a generate would produce

      - This is the type of electricity in your house

- Energy that is pushing the electrons is potential difference

  - Potential difference in energy is either when there is a lot of electrons built up in one place or there are positive and negative plates

    - This is measured in potential energy/ coulomb

      - Or since the unit for energy is the joule, it is joules /coulomb

    - The unit for potential difference in electricity is the volt

      - So one volt = joule/coulomb

- Resistance is the opposition to the flow of  electrons and is measured in ohms (Ω) after the Swiss Scientist George Ohm

  - All matter resists the flow of electrons to a certain degree

  - Ohms Law states current is equal to potential difference divided by the resistance

    - Current = voltage/resistance,  I = v/R, or V=IR

    - A conductor that has a large resistance for its size is called a resistor

  - Sometimes it is helpful to think of electricity a little like water.

    - In this comparison:

      - Current is like the amount of water that runs/minute

      - Voltage is like the amount of pressure the water has

      - Resistance would be like the size of the hose/pipe that you are running water through

- Circuits are a path that electricity follows

  - Parts of a circuit

    - Switch is something that connects or breaks the circuit

    - Wire

    - Resister

    - Power source

      - Battery

      - Generator

  - Two types of Circuits

    - Series Circuit has only one path for current to flow

      - Current is the same throughout the circuit

      - As energy passes through each appliance in a circuit some energy is lost

    - Parallel circuits has more than one path for electricity to flow

  - Circuit diagram shows the difference parts of a circuit

  - Fuses and breakers

    - Fuses are devices connected in series with appliances that melt if to much current runs through

    - Breaker is a device that will shut off if to much current runs through it.

- Power

  - Anything that does work in a certain period of time is called power and is measured in watts

  - To find the power in a circuit multiply the number of volts times the number of amps

    - Volts X  Amps  =  Watts

  - Calculating electric energy used

    - A watt hour is equal to one watt of power used for an hour

  - A kilowatt hour is equal to 1000 watts being used for an hour