Chapter 6

Using Thermal Energy

- Moving of thermal energy

  - Conduction -  transfer of energy by direct contact of matter

    - Result of one particle colliding with another

    - Conduction takes place best when particles are close together

      - Some solids are better conductors than other.

  - Convection -  energy transfer by the movement of matter

    - The difference between conduction and convection is that in convection the particles move from one place to another and conduction the particles remain in approximately the same place

    - Convection is in a fluid where particles can move

      - Water and air

      - Hot air balloon

      - Cause of ocean currents

      - And wind

  - Radiation -  Transfer of energy in the form of waves

    - The absorbed radiant energy is turned to thermal energy

    - Some energy is reflected

      - Different material absorb energy different

        - Shiny reflect radiant energy

        - Dark absorb radiant energy

      - Anything above 0 Kelvin emit radiation

  - Insulators do not allow heat to move easily

    - Insulators are usually a combination of air pockets and reflective material

      - Air pocket stop or slow conduction and convection

      - Reflective surfaces help stop radiation

    - Types of insulators

      - Wood, plastics, glass, foam

    - Insulation ratings

      - R values are the resistance to heat flow

        - R value is the resistance of 1 m by 1 m of material for each cm thickness

        - R value needed in the wall is 19 and in the roof is 30-40

        - Windows have a low R factor

      - R value table p 157

- Using heat

  - Convection heating systems

    - Radiator systems

      - Radiator is a device with a lot of surface area designed to heat the air near it by conduction

      - Convection currents then circulate the heat in the room

      - Usually hot water or steam but can be electric

    - Forced Air – Overhead

    - Electrical heating systems

      - Some use conduction and radiation to create convection currents

  - Solar Heating

    - Use of the sun to heat the building

      - Passive solar heating

        - Uses no fans or mechanical devices to move heat

      - Active solar heating

        - Uses fans, pumps or whatever is needed to move energy to the building from the solar collector

- Using heat to do work

  - Heat engines are devices that convert thermal energy into mechanical energy

  - Internal combustion engines

    - Fuel is burned inside the engine to expand the air to do the work

      - Diesel

      - Gasoline

  - External combustion engines- fuel is burned outside engine to cause expanding gases to move piston or turbines

- Heat movers -  a device that moves heat from one place to another

  - Refrigerator

  - Air Conditioner

  - Heat pump

  - Sweat the human heat mover