Review Sheet

Physical Science Chapter 21

# Name ________________________

Know your vocabulary!!!

Short Answer & Fill in the Blank:

- Current that does not reverse direction is ________________ current.

- How do alternating current differ from direct current?

- What is a coulomb?

- What is static electricity?

- What is electric current and what is the unit for electric current?

- What is potential difference and what is the unit for potential difference?

- What is resistance and what is the unit for resistance?

- What is the current if the voltage is 110 and the resistance is 20 ohms?

- What is the difference between a parallel and a series circuit?

- How does a circuit breaker work?

- What is the unit of electric power?

- What is the unit of electricity used by the power company to measure the amount of electric energy used by a home or business?

- If the hair dryer that you use to dry your hair draws 5 amperes and is plugged into a 110 volt outlet, how much power is required to operate the hair dryer?

- Which figure is a parallel circuit?

Find the missing value in each problem. Be sure to use the correct units in your answers.

- A radio operates with a potential difference of 9 volts. The radio uses 0.9 watt of power. How much current does the radio use?

- A blow dryer uses 1200 watts of power. Current flow through the blow dryer is 10 amperes.   At what potential difference does the blow dryer operate?

- A lamp operates with a potential difference of 120 volts and a current of 0.25 ampere. How much power does the lamp use?

- A lamp uses 60 watts of power. It operates with a potential difference of 120 volts. How much current does the lamp require?

- A small electric furnace that expends 2.00 kW of power is connected across a potential difference of 120 V.

  - What is the current in the circuit?

  - What is the resistance of the furnace?

  - What is the cost of operating the furnace for 24.0 h at 7.00 cents/kWh

Matching:

## Column I

_____ 1. Potential difference

_____ 2. Current

_____ 3. Electric power

_____ 4. Electrical energy

_____ 5. Resistance

## Column II

a. W or kW

b. (Ω)

c. V

d. kWh

e. A

Equations:

V= IR

VI =P